# A Replacement Standard for the CAMAC System in the LLR

Hartebeeshoek Radio Astronomy Observatory

Space Geodesy Programme

Author: Tamsen Emmerich

Date: 04/ 11/2010

This report compares data acquisition modules for the CAMAC replacement in the LLR. Three I/O module bus standards are presented and compared in a decision matrix. They are PCI, VME and Ethernet. Important aspects like bus speed, determinism, prices and availability are also examined and differences between serial and parallel busses are presented. Lists of vendors and examples of I/O modules are included in the appendices.

Contents

1. Introduction									2

2. Some Important Bus features							2

2.1 Bus Speeds; Latency and Bandwidth					2

2.2 Availability								3

2.3 “Real Time” or Deterministic Systems					3

2.4 Software Compatibility							4	2.5 Serial versus Parallel Busses						4

3. LLR System Design								4

4. Three Bus Standards								5

4.1 VME									5

4.1.1 VME Speed								5

4.1.2 VME I/O Module Availability					5

4.2 PCI									6

4.2.1 PCI Speed								6

4.2.2 PCI I/O Module Availability						6

4.3 Ethernet									6

4.3.1 Real Time Ethernet							6

4.3.2 Ethernet Speed							7

4.3.2.1 Latency Calculation Example				8

4.3.3 Ethernet I/O Module and Switch Availability				8

5. Decision Matrix									9

6. Discussion									10

7. Conclusion									10

Appendix A										І

Appendix B										VI

Appendix C									          XII

1. Introduction

HartRAO is in the process of developing a Lunar Laser Ranger (LLR) and will be using the MOBLAS Satellite Laser Ranging (SLR) system as a starting point for the design . As part of this work, the outdated CAMAC crate SLR subsystem needs a suitable replacement standard.

CAMAC, Computer Automated Measurement and Control, is a 1969 IEEE-standard for data acquisition and control systems. It is modular and real-time and was a high-performance system for its time [2]. The SLR uses a CAMAC crate as the major, real time interface between a control computer and the rest of the system. Its modules include; digital I/O’s, ADC’s, DAC’s and a high-speed A/D input multiplexer [3].

Various I/O standards followed, after CAMACs introduction, and many have subsequently disappeared [4]. However, bus standards that have been successful include; VME, PCI, USB, ISA, GPIB and SCSI. All of these support centralized system designs whereas Ethernet is becoming increasingly popular for distributed systems [5].

The most important considerations, for choosing a CAMAC replacement, are bus speed, availability, price and software support. For LLR it is also important that the bus supports a deterministic or “real-time” system. Based on these criteria, three bus standards were selected for comparison. They are; PCI, VME and Ethernet.

This document presents a comparison between these three bus standards. The importance of the bus feature of; speed, availability, determinism, and software support as well the difference between serial and parallel architectures, are first discussed. Some general system designs are then put forward before the three busses are presented in tern. A decision matrix is included, for ease of comparison, thereafter the results are discussed and finally the report is concluded.

2. Important Bus Features

2.1 Bus Speeds; Latency and Bandwidth

The speed and capacity of a bus or network are defined by latency and bandwidth respectively. Latency is the amount of time it takes information to travel from its source to its destination and is often quoted in milliseconds. Bandwidth on the other hand is a measure of the capacity of the network and is quoted in bits per second.

Bandwidth can always be increased by increasing the number of data lines whereas latency is more difficult to improve.

For the LLR bus, both latency and bandwidth are important. Inputs and outputs from the control computer need to be as fast as possible, thus high latency is needed, but high data throughput is also important, for example from optical sensors. It is also important to note that a system can only react as fast as its slowest component. Because of this, there is little point in using supper fast I/O components, in the LLR, unless the motherboard can also operate at those speeds.

Below is a graph comparing latency and bandwidth in different busses. Some of the data points are out of date or quoting only specific subtypes of the busses. For example 10 Gigabit Ethernet can have much improved latency if time triggered switching is used. Keeping that in mind, the graph can be a useful tool for comparison.

Fig 1: Bus Bandwidth versus Latency [6]

PXI and VXI are form factors of PCI and VME respectively and GPBI stands for General Purpose Interface Bus. For a description of the Ethernet, VME and PCI busses see Section 4.

2.2 Availability

A feature of any good design is maintainability. For the bus standard, maintainability is dependent on the availability of replacements modules. One way to gauge how easily components will be sourced in future is through the number of current vendors/manufactures offering those components. Care must also be taken that products are inter-vendor compatible.

The range of modules available is another important aspect for the bus selection. Analog and digital I/O boards as well as ADCs, DACs, multiplexers and instrumentation all need to be available. In addition, a range of speeds, prices and software support, is also important. All of these choices facilitate a cheaper, more customized system design.

2.3 “Real-Time” or Deterministic Systems

Loosely speaking, a deterministic system is a system whose state can be predicted. This includes the predictability of the time delays between an input to the system and its output. A real-time system, on the other hand, is a system in which the time delay is specified within limits. Hard real-time systems guarantee that a response will happen before a deadline whereas soft real-time systems tolerate a degree of lateness. For the purpose of this bus comparison, real-time will refer to hard real-time.

The LLR system has both; a controlling subsystem, including for safety equipment, and a precision timing subsystem, to picosecond accuracy. Both these subsystems are time-critical and thus need to be deterministic. As an interface between the controlling computer and the rest of the system, the CAMAC crate replacement must also therefore have a level of determinism in its data transfer capabilities.

Note: Programmable Logic Controllers, PLCs, are rugged, real-time system controllers used in Industrial Measurement and Control. They have almost all the input/output functionality and software support necessary for the CAMAC replacement. However, traditionally, they have very limited data logging capabilities. That being said, these two fields (Industrial Measurement & Control and Data Acquisition) are steadily converging.

2.4 Software Compatibility

For easier implementation, a range of standard software support is necessary for the I/O bus modules. This range often has more to do with the specific manufacturers rather than the bus standard itself. All three bus standards, compared in section 4&5, are sufficiently universal to have a range of manufacturers offering standardised software support. This support includes; Matlab, C, C++, LabView, Visual Studio, etc.

The I/O module’s software support also needs to be compatible with the chosen operating system, OS. This OS could be a standard type like Microsoft Windows, open source like Linux or even a real-time OS.

2.6 Serial versus Parallel Busses

Serial communication is the process of sending packets of data down channels, one bit at a time. In contrast, parallel communications send several bits at once, down parallel channels. In addition to this, parallel and serial bus module designs are different in that the parallel bus modules share lines whereas the serial ones have dedicated lines. This point-to-point serial architecture can however cause complexities unless switching is used [7, 8, 9]

Crosstalk and clock skew have limited parallel signalling to 1 GHz. Thus, in order to go faster, manufacturers have migrated to serial busses. These busses also have added advantages arising from the reduced number of signal lines. These advantages include higher system density and lower costs because of the reduced pin count.

Latency calculations for serial and parallel busses are different. The calculations are more complex for serial busses. The following formula can be applied:

Serial latency = # of clocks to deserialize + deskew + memory latency + # of clocks on the first bit out [10].

3. LLR System Design

The LLR system design could incorporate subsystems with varying degrees of determinism. A selection of different bus standards suited to the specific application could thus also be used. Such a hybrid system design could have cost and flexibility benefits. To find out if this type of system design is viable, the cost of bus to bus interface cards and using more expensive, hard real-time boards for non-critical systems, would have to compared.

Another design choice is between a distributed system or a centralized one. A distributed system has measurement and control subsystems as close to their sensors and actuators as possible. A centralised system on the other hand has one central control hub. This design choice affects the bus choice in that a distributed system needs a bus that can transport signals over longer distances. Additionally, if the design allows it, a distributed system could handle all time-critical operations at the sensors or actuators allowing a soft real-time bus standard.

4. Three Bus Standards

4.1 VME

Versa Module Europa, VME, was introduced in 1981 [11]. It is an asynchronous, parallel bus, available in 16 to 64 bits and there are more than 300 manufacturers of VMEbus products worldwide [12].

VME is a backplane interface bus with three main types of cards; the Controller, which supervises bus activity, a Master which reads/writes data to a Slave board, and a Slave interface which simply allows data to be accessed via a read/write from a Master. [13].

The VME bus has reached its speed limit. Its potential successor, VPX, has moved from a parallel bus backplane to a switched serial backplane. It uses protocols such as PCI Express, Serial Rapid IO and 10 Gigabit Ethernet [14].

The open VPX standard is still in development thus there are some interoperability issues between vendors.

4.1.1 VME Speed

Data travels along a VMEbus in parallel rather than a few bits at a time but transfer speeds top out at around 320 Mbytes/s – some say 500 Mbytes/s [14].

VME features variable speed handshaking protocols so the bus latency is adjustable and each system’s latency is therefore unique [15].

4.1.1 VME I/O Module Availability

VME manufacturers have 30 years of experience and, even though VME has reached its speed limit, new improved modules are still being developed. There are a wide range of VME I/O modules available and, as mentioned before, there are over 300 manufacturers of VME products but, unfortunately, oscilloscopes and timer/counters are only available from a few companies.

Form factors are of the Eurocard design and three card heights are allowed with VME; 3U, 6U, or 9U. Length is either 160mm or 340mm (Norm) [13].

4.2 PCI

The Peripheral Component Interconnect, PCI, bus standard was introduced in 1992. It is an intermediate bus, located between the processor bus and the I/O bus and is used for attaching hardware devices in a computer. These devices can either be integrated circuits or expansion cards [16, 17]

PCI allows bus mastering which enables devices connected to the bus to initiate transactions [18].

The serial PCI Express, PCIe, bus was created in 2004. It is software backwards compatible with the PCI but allows for much grater speeds. PCIe is particularly popular as a graphics card interface.

4.2.1 PCI Speed

The PCI bus revision in 2002 specified a bandwidth of 264 Mb/s, for the 32 bit and 66 MHz form [16, 17].

PCI bus latency is determined by bus transaction protocol. Because PCI’s serial architecture forces devices to share the bus, a function called an arbiter is needed to determine which device will be allowed to master the bus next. The arbiter uses the maximum latency register, present on the I/O modules, to determine priority levels. Each device also has a register, called the latency timer, which specifies the minimum time the device will have control for [19].

For a single lane (x1), PCIe 1.0 has a bandwidth of 2 Gb/s (250 MB/s) and PCIe 2.0 has twice that. This was achieved by doubling the base clock speed from 2.5 GHz to 5 GHz.

PCIe encoding consumes 20% of available bandwidth (already taken into account of 250 MB/s bandwidth) and signal priority is determined by traffic class [20].

4.1.1 PCI I/O Module Availability

PCI and PCIe bus I/O modules are available in a variety of form factors; CompactPCI  Express, Mini PCIe, ExpressCard, ExpressModule, AdvancedTCA and Cable/Socket boards [7*]. Of these the most widely available, for data acquisition, are the Compact PCI (cPCI), PXI and standard PCIe and PCI. Most of the above are also available in U3 (32 bits) or U6 (64 bits).

PCI eXtensions for Instrumentation (PXI), is a rugged PCI form factor that gets plugged into a chasse. It is supported by over 70 manufacturers and has a wide range of modules including controllers with their own OSs. A PXI chasse also has all the standard input ports for computer mice, keyboards and monitors.

PXI Express is the equivalent form factor for PCIe.

In the most widely available form factors, there is a sufficiently wide variety of I/O modules for the LLR. There are also oscilloscopes available although the PCI forms have a wider range than the PCIe.

4.3 Ethernet

Ethernet is the major local area network technology. Because of this, Ethernet products can take advantage of economies of scale, i.e. low prices. Ethernet bandwidth has also, thus far, followed Moors law. It is now in the 10 Gigabit range and, due to switching, Ethernet has become more deterministic. The use of Ethernet in real-time data acquisition systems is therefore steadily increasing.

Ethernet is also suited to more distributed systems. For instance, a single CAT 5E cable can reach 100 m before needing a switch or router to carry the signal farther [21].

4.3.1 Real-Time Ethernet

Full duplex (bidirectional), switched Ethernet has opened up the possibility of using Ethernet for real-time, critical applications. However, two main concerns remain: 1) the un-deterministic nature of the Ethernet, with does not guarantee the real-time response to a system request and 2) the potential corruption of data, or loss of packets, due to large and sudden increase of traffic [22]. To combat this, the following Ethernet switch specifications are needed:

- 100Mbps, or above, port speed

- Full Duplex

- Priority Queues

- Virtual LAN

- Loss of link management

- Rapid Spanning Tree Protocol

- Back-pressure and flow control

- IGMP snooping and multicast filtering

- Fibre optics port interface

- Remote monitoring, port mirroring and diagnostics

- Extended temperature range and EMI hardened [22]

A real-time Ethernet network cannot guarantee an exact latency. However, the worst case latency can be estimated. This is done by adding up all the worst case time delays in the system. For instance, Woven Systems has quoted a worst case latency of 1.5 μs, for a single switch network [23].

4.3.2 Ethernet Speed

Ethernet is available in bandwidths up to 10 Gigabits and vendors are preparing to demonstrate 100 GigabitE [24].

The latency of an Ethernet network depends on the Ethernet switches used and the amount of data throughput. As an example, see the graph below. Also see the latency calculation example that follows.

Fig 2: Round Trip Latency vs. Data Throughput [25]

4.3.1.1 Latency Calculation Example

Take latency, in a switched Ethernet network, to be the time from when the first packet bit is clocked out, onto the Ethernet transfer link, until the last bit is clocked in, on the receiver link. In order to calculate this latency, the following need to be added.

- Time to transmit all bits from the device to the input FIFO of the switch port

- Time to write the packet data into the switch memory

- Time to perform a lookup (operates in parallel to data storage therefore not added)

- Time to read the packet from the data memory

- Time to transmit the packet [26]

4.3.3 Ethernet I/O Module and Switch Availability

- There are at least 39 manufacturing companies offering Ethernet switches. These companies supply; Data Acquisition and control, Industrial Automation & Control and Data Centres. See Appendix A, table 4, for a list.

- Ethernet I/O modules and controllers have at least 5 manufacturing companies.

- Ethernet cables are freely available.

LXI is a form factor like PXI and VXI but for Ethernet/LAN. It also has all the I/O modules, needed for the LLR, including oscilloscopes. There are over 50 manufacturers supporting this range, see Appendix A, table 2.

5. Decision Matrix

Below is a decision matrix comparing the three busses presented in Section 4. The matrix attempts to compare; the prices, bandwidth, latencies and availabilities of the I/O modules.

Some of the comparisons, for instance latencies, do not have values included. This is because there is no fixed answer.

- Latencies are dependent on cable length, system module number, logic type, switches and frequency choice, to name a few.

- Module numbers/ranges are dependent on the form factor chosen

- Prices are dependent on; form factor, ruggedness, vendor, speed, accuracy and input and output number

The manufacture numbers, quote only those that were found. There could be significantly more. Also take into account that an Ethernet solution for the LLR will need switches as well as I/O modules. To see lists of the manufacturers found refer to table 2 and 3, in Appendix A. Manufacturers for Ethernet switches are in table 4.

Bandwidths are specific to the form indicated. VME and PCI are both also available in 64 bits, which has double the bandwidth of the 32 bit forms. Similarly PCIe (×4) has four times as much bandwidth as (×1).

As far as oscilloscopes, the biggest factor is availability. For instance, ZTECH offers a range of oscilloscopes which are offered in PCI, PXI, LXI and VXI, all at the same price.  For a few oscilloscope vendors, see table 5 in Appendix A.

Table 1: Bus Decision Matrix

For some examples of the I/O modules available, see Appendix B.

6. Discussion

The choice of bus standard is a trade off. Ethernet has the highest bandwidth, PCIe has the lowest latency and VME is the most tried and tested.

All the bus standards compared appear to have enough manufacturer support for maintainability. Similarly good software support is available from the right vendors.

PCI is likely the best choice of bus for the LLR because it is real-time, has the widest manufacturer base and is available at good prices. Unfortunately its bandwidth is not as high as PCIe.

More work is needed to determine exactly which form factor should be used and will be largely dependent on the choice of vendor. There is a table in Appendix C which lists some issues to look out for from PCI manufacturers.

7. Conclusion

Three bus standards, for the LLR system’s data acquisition boards, have been compared. They were PCI, VME and Ethernet. Important bus features where examined. Thereafter, each bus was presented and then compared in a decision matrix. In the discussion, it was concluded that the PCI bus is likely the best bus for the LLR system. The material collected so far is however inconclusive as to which form factor to use.

# References

[1] Space Geodesy, HartRAO, Lunar Laser Ranger, http://geodesy.hartrao.ac.za, last updated on 2008/11/20

[2] Kinetic Systems Corporation, United States, Products, CAMAC, http://www.kscorp.com/Products/camac/display/index.htm, last accessed October 2010, © DynamicSignals LLC 2009

[3] Mobile Laser Ranging System, Stations -4 Through -8, Technical Manual, revision 1, NASA, Goddard Space Flight Center, Greenbelt Maryland, July 1997

[4] THE EXPERIENCE OF USING CAMAC PRODUCTS IN ACCELERATOR

CONTROL, T. Huang, Institute of Modern Physics, Chinese Academy of Sciences and G. Zhang, Department of Computer Science, Lanzhou University, International Conference on Accelerator and Large Experimental Physics Control Systems, 1999, Trieste, Italy.

[5] LXI Strategy, Crystal Instruments, Services, Hardware Development, www.go-ci.com, Copyright © 2010 Crystal Instruments Corporation.

[6] Selecting the Right Bus for Your Digitizer/Oscilloscope Application, NI Developer Zone, http://zone.ni.com/devzone, last accessed 21/10/2010.

[7] PCI Express High Level Overview, Jawaid Ahmad, Texas Instruments, Developer Conference, March 7-9 2007, Dallas Texas.

[8] VXS for VMEbus Embedded Systems, Roger H. Hosking, Pentek, Evaluation Engineer, Data Acquisition, http://www.evaluationengineering.com , May 2005

[9] Serial Communication, http://en.wikipedia.org/wiki/Serial_communication, last modified on 27 October 2010 at 05:44.

[10] High-Speed Serial Memory Interfaces, Michael Miller, http://www.chipestimate.com, Copyright © 2010 MoSys, Inc

[11] Motorola, Years in VME Market, http://vmenow.com, April 2006, last accessed 21/10/2010.

[12] What Is VME, VME Critical Systems, http://www.vmecritical.com/magazine, last accessed 21/10/2010.

[13] VME bus, http://www.interfacebus.com, © 1998 - 2010 All rights reserved Leroy Davis, Modified 9/2/10.

[14] Move Over VME, pg 24, Avionics Magazine, July 2010

[15] New Trends With VME and VPX, A historical perspective with a look at the future, Speaker: Pierfrancesco Zuccato, Eurotech, Boards & Solutions Conference 2010.

[16] PCI Bus, Kioskea net, http://en.kioskea.net/contents/pc/pci.php3, last update on Thursday October 16, 2008

[17] Conventional PCI, http://en.wikipedia.org/wiki/Conventional_PCI,  last modified on 28 October 2010 at 19:57.

[18] PCI Bus Overview, Technical Support, Quatech © 2009, http://www.quatech.com/support/comm-over-pci.php, last accessed 05/11/2010

[19] How The PCI Bus Works, TechPro.net, © 2010 Tech-Pro, http://www.tech-pro.net/intro_pci.html, last accessed 05/11/2010.

[20] Overview of PCI Express, National Instruments, http://anirbanexpertconsulting.com/Overview_of_PCI_Express.pdf, last accessed 2 November 2010.

[21] Simple, Complete Ethernet Data Acquisition, National Instruments, NI Development Zone, © 2010 National Instruments Corporation, last accessed 26/10/2010.

[22] “Modern Industrial Ethernet Switches Can Be Deterministic & Real Time Responsive”, Steve C. Tang, Sr. Staff Engineer, Victor K. Liang, V.P. Marketing, TC Communications Inc, www.JumboSwitch.com, 9/5/2008

[23] 10 GE Fabric Delivers Consistent High Performance for Computing Clusters at Sandia National Labs, http://www.chelsio.com/sandia_benchmark_tech.html, © Copyright 2010 Chelsio Communications

[24] 100G Ethernet moves forward, Rick Merritt, EE Times Asia,11 Oct 2010

[25] 10G Ethernet: The Foundation for Low-Latency, Real-Time Financial Services Applications and Other, Future Cloud Applications, Bruce Tolley, PhD, Solarflare Communications, http://www.solarflare.com/technology/documents/AristaSolarflare_LowLatency10GigEthernet.pdf, last accessed 25/10/2010

[26] Switched Ethernet Latency Analysis, GE Fanuc, Intelligent Platforms, www.gefanuc.com, © 2009 GE Fanuc Intelligent Platforms, Inc. All Rights Reserved.

# Appendix A

The manufacturers listed in the following tables were found on the internet. There are likely many other manufacturers producing VME, PCI and Ethernet boards.

Table 2: PXI, LXI and Compact PCI Manufacturers

| PXI | Compact PCI | LXI |
| --- | --- | --- |
| ADLINK | AIM GmbH | Agilent Technologies |
| Aeroflex | Alta Data Technologies LLC | Pickering Interfaces Ltd |
| Agilent Technologies | Agilent Technologies | Rohde & Schwarz GmbH & Co KG |
| AIM-USA | Alpha Data | Aeroflex, Inc. |
| Bloomy Controls (USA) | Alphi Technology Corp. | AMETEK Programmable Power |
| Chroma Systems Solutions | Ballard Technology | Bruel & Kjaer S & V |
| CHROMA ATE | BittWare Inc. | C & H Technologies, Inc. |
| Corelis Inc | BVM | EADS North America Defense |
| Conduant Corporation | Carlo Gavazzi | Giga-tronics Incorporated |
| Data Device Corp | CES | Keithley Instruments, Inc. |
| Dow-Key Microwave Corp. | Computer Modules Inc | National Instruments Corporation |
| DGE, Inc. | Curtiss Wright | Proft InFocus, LLC |
| EADS North America Test & Services | Diversified Technology 'DTI' | Tektronix |
| Gage Applied Technologies | DSS Networks | The MathWorks, Inc. |
| Geotest | Dynamic Engineering | VTI Instruments Corporation |
| GOEPEL electronic | esd gmbh | Wheelwright Enterprises |
| Gespac | Excalibur Systems | GOEPEL Electronic GmbH |
| Giga-tronics | Extreme Engineering Solutions | TDK-Lambda Americas Inc. |
| JTAG Technologies | GE Fanuc | ZTEC Instruments |
| KineticSystems | General Standards Corp. | AAI Corporation |
| Konrad Technologies | Gespac | Acery Technologies Co. Ltd. |
| LeCroy | Get Engineering Corp. | ARC Technology Solutions |
| Meilhaus Electronic Gmbh | Innovative Integration | Beijing Control Industrial Computer Corporation |
| MEN Mikro Elektronik | INTERFACE CONCEPT | Beijing Aerospace Measurement & Control |
| MAC Panel | Kontron | Bustec |
| National Instruments | Mercury Computer Systems | Chroma ATE Inc. |
| OpenATE | One Stop Systems Inc. | Circuit Assembly Corp. |
| Phase Matrix | PCI Computer Systems | Data Physics Corporation |
| Pickering | Performance Tech | Data Translation |
| PLX Technology | Raytheon {cPCI boards} | DowKey Microwave |
| PXIdirect | SeaLevel Systems Inc. | GE Druck |
| Ranatec Instrument AB | Spectrum Signal Processing | Good Will Instrument Co., Ltd. |
| SP Devices | Symmetricom | Hitech Group International, Ltd |
| Spectrum GmbH | Twin_Industries | Holding Informtest |
| Strategic Test AB | Znyx Networks | JDS Uniphase Corporation |
| Sundance |  | Kepco, Inc. |
| TEGAM |  | Kikusui Electronics Corporation |
| Teradyne |  | LeCroy |
| Tracewell Systems |  | LXinstruments GmbH |
| Tundra Semiconductor Corporation |  | Magna-Power Electronics Inc. |
| Virginia Panel |  | Micrel Semiconductor, Inc. |
| ZTEC |  | NF Corporation |
|  |  | NPP MERA |
|  |  | Picotest Corp. |
|  |  | Rigol Technologies, Inc. |
|  |  | TEGAM |
|  |  | Teradyne |
|  |  | TTi Ltd. |
|  |  | Tyco Electronics |
|  |  | Universal Switching Corporation |
|  |  | Yokogawa Electric Corporation |

Table 3: VME, VPX and VXI Manufacturers

| VME | VPX | VXI |
| --- | --- | --- |
| Acromag | Bustronic Corporation | AIM GmbH |
| AcQ InduCom | Curtiss Wright | Agilent Technologies |
| Act/Techno | Extreme Engineering Solutions | Bustec |
| AIM GmbH | GE Fanuc Embedded Systems, Inc. | C&H Technology Inc. |
| Aitech Defense Systems Inc. | General Dynamics, Canada | EADS North America Defense Test and Services, Inc. |
| Alacron Technology | Interface Concept Inc. | Excalibur Systems |
| Alpha Data | Mercury Computer Systems | Frequency Devices |
| Alphi Technology | North Atlantic Industries | Giga-Tronics |
| Ballard Technology | PCI Embedded Computer Systems | GE Fanuc |
| Bi Ra Systems |  | Highland Technology |
| Bustronic Corporation |  | Holding "Informtest" |
| CAEN Technologies Inc |  | ICS Electronics |
| CM Computer |  | KineticSystems |
| CompControl |  | National Instruments Corp. |
| Concurrent Technologies Inc. |  | North American Instruments Inc. |
| Control Sciences Inc. 'CSI' |  | Phase Matrix Inc. |
| Curtiss Wright |  | REC Test |
| Data Device Corporation "DDC" |  | Spectral Dynamics, Inc. |
| Dawn VME Products |  | Symmetricom |
| esd gmbh |  | Teradyne |
| Extreme Engineering Solutions |  | Tracewell Systems |
| Frequency Devices |  | Virginia Panel Corp. |
| Galil |  | VXI Technology |
| GDP Space Systems |  | VTI Instruments |
| GE Fanuc |  | WIENER, Plein & Baus Corp. |
| Get Engineering Corp. |  | ZTEC - Gary Tilley |
| Highland Technology |  |  |
| Hewlett-Packard Co |  |  |
| Interface Concept |  |  |
| MacroLink Inc. |  |  |
| Mercury Computer Systems |  |  |
| N.A.T. |  |  |
| National Instruments |  |  |
| North Atlantic Industries |  |  |
| Nyden |  |  |
| Robotrol Corp. |  |  |
| Sabtech Industries |  |  |
| Sky Computers |  |  |
| Spectrum |  |  |
| Symmetricom |  |  |
| Twin_Industries |  |  |

Table 4: Ethernet Manufacturers

| Switches | Controllers | I/O Modules |
| --- | --- | --- |
| 3Com | Galil | Acromag |
| ACKSYS | EtherCAT Technology Group | DataTranslation |
| Advantech | PMC Corp | Gefran |
| Astro-Med | Scheider Electric | Mosaic industries |
| Atheros | Performance Motion Devices | Scheider Electric |
| atop | Parker Hannifin | ICP DAS |
| Bachmann | Vital Systems | Contempory controls |
| B&B electronics | Active Robotics |  |
| Comtrol | Baldor |  |
| Contempory controls | National Instrument |  |
| Dell | Turck |  |
| Elma | Intelligent Instruments |  |
| EKS | Baldor |  |
| Ethernet Direct | Data Translation |  |
| Fujitsu | Intelligent Instrumentation |  |
| Gantner | Super Logistics |  |
| GE Fanuc | QSI Corp |  |
| GarrettCom | Moxa |  |
| Hartings | PMC Corp |  |
| Hirschmann | The Vision Depot |  |
| ICP DAS | Arista |  |
| Innominate | Moeller |  |
| Korenix | QSI Corp |  |
| Kyland | Red Lion |  |
| Luceat | Beckhoff |  |
| Lutze | Interweigh systems Inc |  |
| Moxa | Maple systems |  |
| molex | Dataq Instruments |  |
| Myricom | National Instrument |  |
| N-Tron | Red Lion Controls |  |
| Oring | G&L Motion control |  |
| Performance Technologies | GE Fanuc |  |
| red lion | Nematron |  |
| Ruggedcom | Acromag |  |
| Siemens | Mosaic Industries |  |
| Sixnet | eZE System Inc |  |
| Weidmuller | Gefran |  |
|  | Cas Datloggers |  |
|  | ABSS Co |  |
|  | Identec solutions |  |
|  | Schneider Electric |  |
|  | Pro-Dex |  |

Table 5: Some Oscilloscope Manufacturers

| Company | Busses |
| --- | --- |
| Aquitek | USB |
| Agilent Technologies | PCI, PCIe, cPCI, and VME |
| Ztech | PCI, PXI, LXI, VXI |
| TiePie | PXI, USB |
| Gage Applied Technologies | PCI, USB |
| Meilhaus Electronics GmbH | USB |

# Appendix B

This appendix gives some examples of I/O Data Acquisition modules available. These tables are not intended to be comprehensive; many thousands of other I/O modules are available.

Table 6: Digital Input Output PC Boards

| Company | Bus | Model | Logic | P Sup | Software Support | I # | O # | Features | Price |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ICP DAC | PCI | PIO-D48U | TTL/DTL | 5V | " | 48 | 48 | 0.77us response time and on board timer/counter chip |  |
| UEI | PCI | PDL-DIO-64 | TTL | 5V | PowerDAQ Software for Windows NT/2000/XP and Linux/RTLinux | 64 |  |  | $435.00 |
| UEI | PCI | PDL-DIO-64CT | TTL | 5V | " | 64 |  |  | $1,205.00 |
| UEI | PCI | PDL-DIO-64ST | TTL | 5V | " | 64 |  |  | $1,205.00 |
| UEI | PCI | PD2-DIO-128 | TTL | 5V | " | 128 |  |  | $765.00 |
| UEI | PCI | PD2-DIO-128i | TTL | 5V | " | 128 |  |  | $765.00 |
| UEI | PCI | cPCI64-HPDI32ALT | TTL | 5V | " | 164 |  |  | $435.00 |
| UEI | PCI | PDXI-DIO-64 | TTL | 5V | UEIDaq Framework: with bindings for all major programming languages and data acquisition / test programming environments including C, C++, C#, VB.NET as well as Excel, OPC, MATLAB, DASYLab, TestPoint, Agilent VEE, LabVIEW for Windows and LabWindows/CVI. | 64 |  | 64 digital I/O channels, 3 counter/timers, 2 ESSI ports, 4 high-speed IRQ lines (100 ns) | $435.00 |
| UEI | PCI | PDXI-DIO-64ST | TTL | 5V | " | 64 |  | 64 digital I/O channels, high-speed pattern generation and digital streaming | $1,205.00 |
| UEI | PCI | PDXI-DIO-64TS | TTL | 5V | " | 64 |  | 64 digital I/O channels, high-speed event counts streaming (2 Mwords/s) | $2,415.00 |
| Aquitek | PCI | PMC64-HPDI32ALT | TTL & LVDS | +5.0 VDC | Sample code, Vx Works©, Windows 98©, Windows 2000©, Windows XP©, Linux©, Lab VIEW©, and Windows NT© drivers are available |  |  |  |  |
| MEN | VME | 01a302-ds |  | (+3.3, +5, +24V) | Software Support: MEN Driver Interface System (MDIS™ for Windows®, Linux, VxWorks®, QNX®, OS-9®) | 32 I/O | 32 I/O | 1-slot A24/D16 VMEbus slave, 4 optically isolated units, 32 channels for each unit, Individual use of each channel as input or output, Individual edge-triggered interrupts, Input/output load on ground, High-side output switches, Output current 1.9A per channel or 16A per unit, Over-current and over-temperature protection |  |
| MEN |  | 04m011-co | TTL |  | Driver software for Windows®, Linux, VxWorks®, QNX®, RTX and OS-9® |  |  | 16-bit TTL I/O Interface |  |
| EUROTECH | VME | Advme1209A |  | DC5V±5% | Device driver for VxWorks (option), Sample program | 64 |  |  |  |
| EUROTECH | VME | Advme1211 |  |  |  | 128 |  |  |  |
| GE | VME | VME-1111 |  |  |  |  |  | 64-bit High-Voltage Digital Input VMEbus Board with Built-in-Test |  |
| GE | VME | VME-1150 |  |  |  |  |  | 64-bit isolated Coupled Digital Input VMEbus Board |  |
| GE | VME | VME-2528 | TTL |  |  | 128 I/O | 128 I/O |  |  |
| Xembedded | VME | XVME-240 | TTL |  |  | 64 I/O | 64 I/O | 64 channels (8 ports) of bidirectional TTL I/O, 8 channels of edge-selectable interrupt inputs with programmable mask, 8 channels of flag outputs, High density, low cost-per-channel |  |
| NI | PCI | NI PCI-6503 |  |  |  | 24 I/O | 24 I/O |  | R 1 630 |
| NI | PXI | NI PXI-6608 |  |  |  | 32 I/O | 32 I/O | 8.32bits.80MHz counter/timer | R 24,980 |
| NI | PXI | NI PXI-6508 | TTL/CMOS | 5V |  | 96 I/O | 96 I/O |  | R 5,460 |
| NI | PCIe | NI PCIe-6321 |  |  |  |  |  |  | R 5,460 |
| NI | PXIe | NI PXI-6602 |  |  |  | 32 I/O | 32 I/O |  | R 8,650 |
| NI | PXIe | NI PXIe-6461 |  |  |  |  |  |  | R 13,210 |
| NI | PCI | NI PCI-6221 |  |  |  | 24 I/O | 24 I/O |  | R 5,460 |
| NI | PCI | PCI-6602 |  |  |  | 32 I/O | 32 I/O | 8.32bits.80MHz counter/timer | R 6,830 |
| NI | PXI | NI PXI-6251 |  |  |  |  |  |  | R 10,930 |
| NI | PCI | NI PCI-6601 |  |  |  | 32 I/O | 32 I/O | 4.32bits.80MHz counter/timer | R 3,370 |
| Agilent Technologies | VXI | E1330B | TTL | 5V | Visual Studio®, C, C++, Visual Basic, MATLAB® and LabVIEW™. | 32 I/O | 32 I/O | • 1-Slot, B-size, register based • Quad 8-bit input or output data ports • Interface to industry standard opto-isolator racks • Standard GPIO handshake modes • Wide variety of output data types • Four-port digital input/output module | US$ 1,103 |
| Agilent Technologies | VXI | E1438A | TTL |  | Visual Studio®, C, C++, Visual Basic, MATLAB® and LabVIEW™. | 96 I/O | 96 I/O | * 1-Slot, C-size, register based * Twelve 8-bit input or output data ports for acquisition * Wide variety of output data types * Data port readback on a per-port basis * Control of interface driver tri-state capability * Block mode transfer to/from memory | US$ 2,646 |
| Agilent Technologies | PXI | M9187A | Digital IO |  | Visual Studio®, C, C++, Visual Basic, MATLAB® and LabVIEW™. | 32 | 32 | Applications* For monitoring digital states and controlling external devices Functionality* 32 input channels with programmable thresholds of 0.3V to 50V* 32 output channels with 0.5A low sink/0.4A high source Performance characteristics * 100V input protection* Fully protected outputs* High-quality Dsub connectors | US$ 1,550 |
| Geotest | PXIe | GX 5292e | TTL |  | ATEasy, Microsoft® and Borland® C/C++, Microsoft Visual Basic®, Borland Delphi, and LabVIEW. | 32 I/O | 32 I/O | •32 input / output channels, dynamically configurable on a per channel basis •256 MB of on-board vector memory •Supports 1.5 V, 1.8 V, 2.5 V, 3.3 V, and 5 V TTL/LVTTL interfaces •Supports LVDS, M-LVDS, LVDM interfaces •100 MHz vector rate • x1 and x4 PCI Express interface •Operates as a stand-alone card or with up to seven additional synchronous slave boards | $5,495 |
| Geotest | PXI | GX5641 |  |  | ATEasy, Microsoft® and Borland® C/C++, Microsoft Visual Basic®, Borland Delphi, and LabVIEW. | 64 I/O | 64 I/O | •64 bi-directional I/O channels •Bi-directional TTL I/O and RS422 differential I/O ports per channel •128 digital inputs or outputs with direction control •Channels can be programmed to operate in conversion or static I/O modes through software control •Default direction control per channel via 64 on-board switches •Each TTL and differential output port can be individually enabled/disabled through software control •68-pin VHDCI connectors: two for TTL and two for Differential channels •100-Ohm terminator for each differential I/O signal •Compatible with NI PXI 7811R •GX5641-3 provides 3.3V differential driver | $1,995 |
| Geotest | PXI | GX5641-3 |  |  | ATEasy, Microsoft® and Borland® C/C++, Microsoft Visual Basic®, Borland Delphi, and LabVIEW. | 64 I/O | 64 I/O | " | $3,800 |
| Geotest | PXI | GX5733 | TTL |  | ATEasy, Microsoft® and Borland® C/C++, Microsoft Visual Basic®, Borland Delphi, and LabVIEW. | 96 I/O | 96 I/O | • Three 32-bit TTL ports for a total of 96 TTL input or output channels •One 32-bit configurable port supports 32 TTL channels or accepts one GX57xx I/O module for customized input or output levels •Available I/O modules include Digital Input Latch, Digital Output Latch, Optically Coupled Digital Power Output, Differential TTL (RS-422), LVDS, and input / output modules with vector memory | $649.00 |
| Measurement Computing | PCI | PCI-DIO96 |  |  | TracerDAQ®, Visual Studio® and Visual Studio® .NET, including examples for Visual C++®, Visual C#®, Visual Basic®, and Visual Basic® .NET, DASYLab® and NI LabVIEW™ | 96 I/O | 96 I/O |  | $269.00 |
| " | PCIe | PCIe-DIO96H |  | " | 96 I/O | 96 I/O |  | $399.00 |
| " | PCIe | PCIe-DIO24 |  | " | 24 I/O | 24 I/O |  | $249.00 |

Table 7: DAC and ADC

| Company | Bus | Model | DAC or ADC | Software Support | Ch | Features | Price |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Agilent Tech | VXI | E1328A | DAC | Visual Studio®, C, C++, Visual Basic, MATLAB® and LabVIEW™. | 4 | • 1-Slot, B-size, register based • Four isolated voltage or current DACs • ± 10.92 V or ± 21.8 mA output • Software calibration • Remote voltage sensing with no-fault operation • Multiple channels connected in series/parallel | US$ 2,210 |
| Agilent Tech | VXI | E1418A | DAC | Visual Studio®, C, C++, Visual Basic, MATLAB® and LabVIEW™. | 8 I, 16 O | * 1-Slot, C-size, register based * 8/16 independent channels, flexible and configurable * Individual isolation per channel * 16-bit resolution D/A per channel * Programmable selectable voltage/current modes * Software controlled calibration | US$ 3,328 |

Table 8: Counter/Timers

| Company | Bus | Model | Hz | Res | Software Support | Ch | Features | Price |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Agilent Technology | VXI | E1333A | 1 GHz | 1 ns | Visual Studio®, C, C++, Visual Basic, MATLAB® and LabVIEW™. |  | * 1-Slot, B-size, register based* Six counter functions* 1 GHz frequency measurement * 1 ns time interval/pulse width resolution (avg mode)* Compatible with all Agilent Foundations* Measure time interval between trans | US$ 1,223 |
| Agilent Technology | VXI | E1420B | 200 MHz | 2 ns | Visual Studio®, C, C++, Visual Basic, MATLAB® and LabVIEW™. |  | * 1-Slot, C-Size, message based * 200 MHz frequency range, optional 2.5 GHz channel * 9-digit resolution in 1 second gate time * 2 ns time interval resolution (200 ps with averaging) * Shared memory option configuration * Phase measurement and measurement timeout * For complete details, click on the Data Sheet link | US$ 4,302 |
| Geotest | PXI | GTX2210 | 225 MHz | 500 mVpk-pk at 5 ns pulse width | ATEasy, Microsoft® and Borland® C/C++, Microsoft Visual Basic®, LabVIEW, and Borland Delphi. | 2 I | •14 measurement functions •DC to 225 MHz •Fast measurement mode: 2300 readings/sec •External reference clock input •External arming signal input •Gate signal output •In-system automatic calibration of time base and trigger levels •Automatic trigger level adjustment •Software selectable input impedence (1 MΩ or 50Ω) and coupling (AC or DC) for each input channel | $ 2,150 |
| Geotest | PCI | GC2230 | 2 GHz |  |  |  | •14 measurement functions •DC to 2.0 GHz •100 ps resolution without averaging •Fast measurement mode: 2300 readings/sec •External reference clock input •External arming signal input •Gate signal output •Self-calibration feature ensures highest accuracy •Programmable automatic adjustment of board setting to obtain a stable reading •Software selectable input impedence (1 MΩ or 50Ω) and coupling (AC or DC) for each input channel | $4,150 |
| Keitley | PCI | KPCI-3140 |  |  |  | 8 ch | * 8 counter/timers (16 bit) * 4 interval timers (24 bit) capable of interrupting CPU on timeout * Digital pattern recognition on 8-bit (Port D) * 32 digital I/O lines for high channel count applications * 40MHz clock frequency (max.) * 2-bit DriverLINX® drivers plus bundled start-up software Compatible with TestPoint™ | $495 |

# Appendix C

Table 8: Manufacturer Compliance Issues, Adapted from [18].

| Issue | Importance | Manufacturer Compliance |
| --- | --- | --- |
| All unused 5V and 3.3V power pins are plated on the connector (goldfingers) | Better data integrity because high-speed PCI signals use the power pins for return paths | sometimes, often omitted when "cutting corners" |
| All 3.3V power pins are decoupled from ground with capacitors | Better data integrity because high-speed PCI signals use the power pins for return paths | rare, ground return path capacitors are often omitted |
| All PCI signal lines have one and only one load. (connected to only one pin on one component on the board) | Better data integrity because the PCI bus is extremely sensitive to signal loading | usually, but sometimes violated |
| JTAG boundary scan chain intact if unused (connect TDI to TDO signals) | JTAG boundary scan systems can work with the board installed | extremely rare |
| Trace length of 1.5" or less on PCI signals | PCI signals rely on specific travel times up and down the bus. Proper trace lengths ensure data integrity | usually, but sometimes violated |
| PCI clock trace is 2.5" ±0.1" in length | The PCI clock signal timing is particularly critical. All other PCI signals depend on accurate clock delivery | often violated |
| Full PCI configuration space implemented | So that plug-and-play really works | almost always, but there are some exceptions |